Colinbus main PCB connections
Peter Brier

Top view of mainboard (header pins):

HDR3: 50 pin
HDR2:20 pin
HDR1: 40 pin

HDR1
1	3	5	7	9	11	13	15	17	19	21	23	25	27	29	31	33	35	37	39
2	4	6	8	10	12	14	16	18	20	22	24	26	28	30	32	34	36	38	40

Black = GND
Red = +5V
Green = RS232 (31 = pin3, 32=pin2)
Blue = Limit sensor inputs (18=X, 19=Y, 20=Z) . Switch connects to GND

HDR2
1	3	5	7	9	11	13	15	17	19
2	4	6	8	10	12	14	16	18	20

Yellow: Stepper
Blue: Relay, not connected (16=RY1, 15=RY2)
Red: +5V
Black: GND

3x L6208 Stepper driver connections:
Signal	X	Y	Z	Notes
Enable	6	10	14	Low = off
Step	4	8	12	Rising edge = step
Dir	3	7	11	Low = CCW
Half/Full	+5V	+5V	+5V	Half step
Control	+5V	+5V	+5V	Slow decay
Reset	+5V	+5V	+5V	Low = reset
VrefA	424 mV			Rsens = 0.5 Ohm, / I ~ 1 Amp
VrefB

HDR3
1	3	5	7	9	11	13	15	17	19	21	23	25	27	29	31	33	35	37	39	41	43	45	47	49
2	4	6	8	10	12	14	16	18	20	22	24	26	28	30	32	34	36	38	40	42	44	46	48	50

Pins go to to extension header and other unused parts of the PCB (relay inputs, analog IO, etc)
Black: GND

External D25 connector, connection to LAOS board (TBD

Notes	Name	PIN	PIN	Name	Notes
Motor coil A+	A+	1	14	A-	Motor coil A-
Motor coil B+	B+	2	15	B-	Motor coil B-
24V/1A output	+24VOUT	3	16	OUT3-	Output 3- (collector)
24V/1A output	+24VOUT	4	17	OUT4-	Output 3- (collector)
Ground	GND	5	18	Z+	Input 1- (connect to GND)
Ground	GND	6	19	NC
Ground	GND	7	20	AIN	Analog input (0 .. 5V)
Ground	GND	8
Opto coupler collector	OUT3-C	9	21	OUT3-E	Opto coupler emitter
Opto coupler collector	OUT4-C	10	22	OUT4-E	Opto coupler emitter
CAN High	CANH	11	23	CANL	CAN Low
I2C SCL	SCL	12	24	SDA	I2C SDA
Ground	GND	13	25	+5V	5V

External D9 Connector